## Slide 1
Development of Python-based Toolkit to Improve Analysis of Atom Probe Tomography Data
Vishal Kanigicherla, Dr. Keith Knipling
Thomas Jefferson High School for Science and Technology, U.S. Naval Research Laboratory Materials Science and Technology Division
Figure 5. Programs written to interact with initial raw .pos and .epos data. A major bottleneck with interaction with .pos files is the large amounts of data, often totaling hundreds of millions of atoms to parse. Therefore, optimization and implementation of SQL along with more algorithms are a high priority to moving forward in work on .pos files. The graph is a sample of 10,000 and 100,000 atoms in a sample APT run.
Figure 4. Programs written to interact with proxigram data.
Toolkit Capabilities
Generate initial CSV files from proxigram XLSX.
Take user-input for manual peak decomposition in proxigrams.
Convert proxigram atom counts to at% values.
Generate profiles of proxigram data after discarding irrelevant isotopes.
Create core statistics file from user identification of matrix and precipitate of profile.
Turn large POS files into workable CSVs.
Calculate and display spatial error statistics for proxigram and CSV.
Take inputs for calculating average radius, vol fraction, and number density, do the calculation, and report the uncertainty.
Generate a mass spectrum graph and analysis from POS CSV.
Consolidate programs into GUI using Py2App and tkinter for better user experience.
Calculate statistics such as Gibbsian interfacial excess of solute and distributions of atoms within matrix, precipitate, and core
Figure 3. Image of user interface application with integrated programs. Packages used in this project and thus system requirements are struct, pandas, tkinter, numpy, and matplotlib.

## Slide 2
Citations
Reddy, S. M., Saxey, D. W., Rickard, W. D. A., Fougerouse, D., Montalvo, S. D., Verberne, R., & van Riessen, A. (2020). GGR Cutting‐Edge Review Atom Probe Tomography: Development and Application to the Geosciences. Geostandards and Geoanalytical Research. doi:10.1111/ggr.12313
Lefebvre-Ulrikson, W., Vurpillot, F. & Sauvage, X. (2016). Atom Probe Tomography. London: Academic Press.
Kelly, T. F., & Miller, M. K. (2007). Atom probe tomography. Review of Scientific Instruments, 78(3), 031101. doi:10.1063/1.2709758
Tamura, M., Shukuri, S., Moniwa, M., & Default, M. (1986). Focused ion beam gallium implantation into silicon. Applied Physics A Solids and Surfaces, 39(3), 183–190. doi:10.1007/bf00620733
Dhara, S., Marceau, R. K. W., Wood, K., Dorin, T., Timokhina, I. B., & Hodgson, P. D. (2018). Atom probe tomography data analysis procedure for precipitate and cluster identification in a Ti-Mo steel. Data in Brief, 18, 968–982. doi:10.1016/j.dib.2018.03.094
Vincent, G. B., Proudian, A. P., & Zimmerman, J. D. (2020). Three dimensional cluster analysis for atom probe tomography using Ripley’s K-function and machine learning. Ultramicroscopy, 113151. doi:10.1016/j.ultramic.2020.113151.
Kühbach, M., Breen, A., Herbig, M., & Gault, B. (2019). Building a Library of Simulated Atom Probe Data for Different Crystal Structures and Tip Orientations Using TAPSim. Microscopy and Microanalysis, 1–11. doi:10.1017/s1431927618016252
Knipling, K. E., Narayana, P. U., & Nguyen, L. T. (2017). Microstructures and Properties of As-Cast AlCrFeMnV, AlCrFeTiV, and AlCrMnTiV High Entropy Alloys. Microscopy and Microanalysis, 23(S1), 702–703. doi:10.1017/s1431927617004172
Perea, D. E., Liu, J., Bartrand, J., Dicken, Q., Thevuthasan, S. T., Browning, N. D., & Evans, J. E. (2016). Atom Probe Tomographic Mapping Directly Reveals the Atomic Distribution of Phosphorus in Resin Embedded Ferritin. Scientific Reports, 6(1). doi:10.1038/srep22321
Hellman, O. C., & Seidman, D. N. (2002). Measurement of the Gibbsian interfacial excess of solute at an interface of arbitrary geometry using three-dimensional atom probe microscopy. Materials Science and Engineering: A, 327(1), 24–28. doi:10.1016/s0921-5093(01)01885-8
Krakauer, B. W., & Seidman, D. N. (1993). Absolute atomic-scale measurements of the Gibbsian interfacial excess of solute at internal interfaces. Physical Review B, 48(9), 6724–6727. doi:10.1103/physrevb.48.6724
Acknowledgements
I would like to thank Dr. Keith Knipling of the U.S. Naval Research Laboratory Materials Science and Technology Division for his incredible mentorship in offering resources as an introduction to APT, technology, procedural advice, and constant kind consideration, and guidance during this time. I would also like to thank Dr. Brian Kennedy, the director of the Chemical Analysis Laboratory at Thomas Jefferson High School for Science and Technology, for his patience and support in navigating the mentorship program at Jefferson, among other things. Additionally, I am grateful to Mr. Alfred Lampazzi, the Mentorship Program Director at Jefferson, for making this entire program possible. I have a learned a great deal over the course of this program, and am looking forward to continuing work on this project.
Atom Probe Tomography
Atom-by-atom dissection of a material volume
Sub-nanometer resolution, and chemical sensitivities approaching 10 atomic ppm
Breakdown by field evaporation
Time-of-flight mass spectrometry and impact recordings create reconstruction
Mass-to-charge ratio and (x, y, z) recorded in large binary .pos files
Proximity histogram (proxigram) details at% composition of thin ~.1 nm shells of sample about predetermined surface
Figure 1. The schematics above represent the process of atom probe tomography, and demonstrate how reconstructions can be developed from a position-sensitive detector. Image sourced from Reddy, S. M., Saxey, D. W., Rickard, W. D. A., Fougerouse, D., Montalvo, S. D., Verberne, R., & van Riessen, A. (2020).
The Challenges of Atom Probe Tomography
Leaves molecular artifacts in sample through FIB milling and other processing (Tamura, M., Shukuri, S., Moniwa, M., & Default, M. (1986))
Isotopic overlaps left inherent to time-of-flight mass spectrometry
Mass spectrum ranging and peak identification is difficult
Maximum separation algorithm heavily dependent on user-input parameters, could use optimization (Vincent, G. B., Proudian, A. P., & Zimmerman, J. D. (2020))
Lack of algorithms to calculate error statistics and relevant thermodynamic quantities such as Gibbs interfacial excess of solute for which APT is easily applicable (Hellman, O. C., & Seidman, D. N. (2002), Krakauer, B. W., & Seidman, D. N. (1993))
Large amounts of data make processing generally tedious - optimization and automation of the process is a viable direction for development
Figure 6 . Hellman & Seidman (2002) determined the above formulations that eliminated the need for a priori knowledge of slice area, and through dimensional analysis substituted a formula
Gibbsian Interfacial Excess of Solute
Γs, concentration of solute within an infinitesimally small interface, a “Gibbs dividing surface,” between two bulk phases of a material
Atom probe proxigram data is very well suited for this calculation, already binned shells
Prior formulations require knowledge of area of shell thickness, possible to bypass
Circumvented a priori requisites for ⍴ using lattice parameter of molecular species and assumption of Bravais crystal lattice structure
The purpose of the project was to develop a Python-based toolkit to automate, optimize, and streamline analysis of data produced by Atom Probe Tomography (APT). This project addresses many issues with the raw data and proximity histogram analysis processes conducted after APT, such as the difficulties of mass spectrum peak decomposition, mass spectrum ranging, determining statistics such as Gibbs interfacial excess of solute, and error calculation in reported values.
This was achieved by using established Python libraries such as Pandas to process large amounts of binary data generated by APT into workable CSV files and addressing each issue in APT analysis with discrete scripts, finally compiling them into a toolkit available on Github. In addition to this project holistically addressing APT data analysis using Python and moving APT data analysis away from proprietary software, future goals include improving existing data analysis techniques by implementing various algorithms employing optimization and machine learning.
Project Overview
Figure 2. Unmodified proxigram of atom counts. Note Rn % (27Da), raw data for the 27 Dalton which could be 27Al1+, 54Fe2+, or 54Cr2+. This ambiguity of isotopic overlap requires further resolution, one of the tasks executed by the toolkit. The gallium implanted by FIB milling will also requires resolution by the toolkit
Results and Discussion
The main application interface and related programs can be found at https://github.com/sakanak/apt-csv-work
Current algorithms in the application are those written expressly for the sake of automation of manual tasks, with the exception of the calculation software for the Gibbs interfacial excess of solute
All programs were checked to have complete accuracy through comparison with past files available at the Naval Research Laboratory
The formulation used for Gibbs interfacial excess relies on estimations made for number density using an assumed lattice parameter and structure - further development could reduce such error as proposed in Krakauer & Seidman et al. (1993) for an APFIM TEM calculation of Gibbsian excess
Further Perspectives
A few tasks for the toolkit currently in development include:
  Optimizing cluster detection
  Generating volume and radii calculations with particle info
  Executing peak detection and automatic ranging and isotope assignment using available isotope abundances table
  Modelling matrix composition to track precipitation as a function of time
  Additional tasks are to be determined
Further implementation of different techniques; one example includes utilizing Ripley’s K-function and machine learning to optimize the maximum separation algorithm for cluster detection, while another involves optimizing existing simulations for field evaporation such as TAPSim
Conclusions
Confirmation of the ability of toolkit to automate analysis of data in APT
Implementation of calculators for specific thermodynamic quantities
Identifiable room for development in areas dealing with large amounts of data through implementation of optimization algorithms and different data structures